## Slide 1: Los Angeles Coastal Plain (LACP) Framework Model and Water Budget
Scott Paulinski
This information is preliminary and is subject to revision. It is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.

## Slide 2: Study Area
Los Angeles Coastal Plain (LACP)
~700 square miles of southern Los Angeles and parts of Orange County
Pacific Ocean to the west and south
Santa Monica Mtns and Puente Hills to the north
Orange County to the east
Preliminary

## Slide 3: Study Area
Central, West Coast, Santa Monica, Hollywood basins, and part of Orange County basin
Preliminary
Notes:   Los Angeles Coastal Plain (LACP)
  Pacific Ocean to the west and south
  Santa Monica Mtns and Puente Hills to the north
  Orange County to the east
  Central, West Coast, Santa Monica, Hollywood basins, and part of Orange County basin

## Slide 4: Groundwater History
Heavy pumping from 1940’s through 1960’s
Large groundwater declines
Water supply wells abandoned along coast in early 1950’s due to seawater intrusion
Water Replenishment District of Southern California (WRD) formed in 1959 to protect groundwater resources in Central and West Coast basins
Preliminary

## Slide 5: Groundwater Management
Basin management
  Basin adjudicated, groundwater pumping limited
  Central Basin replenished using spreading ponds along the Rio Hondo and San Gabriel River
  Barrier injection wells near the coast prevent seawater intrusion
Importance of Groundwater in the LACP
  Approximated 5.4 million people living on LACP
  40 percent of water demand is met by groundwater in central and west coast basins
Preliminary

## Slide 6: Pumping/Injection
Most pumping occurs in Central, Orange County, and West Coast Basins
Injection occurs along the West Coast Basin, Dominguez Gap, and Los Alamitos barrier projects
Preliminary

## Slide 7: Study Purpose and Scope
Purpose
  Provide increased scientific understanding of the hydrogeologic system of the Central and West Coast Basins that can be utilized to improve groundwater management
Scope
  Hydrogeologic framework model
  Rainfall-runoff-infiltration model
  Conceptual model and water budget
  Regional three-dimensional groundwater-flow model
Preliminary

## Slide 8: Previous Lithostratigraphic Framework Model
Previous model defined aquifers by their lithology
  Aquifers were generally areas with higher concentrations of gravel and sand
Lithostratigraphic unit
  A body of rocks or alluvium that is defined and recognized on the basis of its lithologic properties (ex. grain size)
  Units may or may not have been deposited at the same time across their spatial extent
Preliminary

## Slide 9: New Chronostratigraphic Framework Model
Ponti and others constructed model using Earthvision
3D model of the entire Los Angeles Coastal Plain
Thirteen layers + basement
Preliminary

## Slide 10: Lithostratigraphic vs. Chronostratigraphic
Chronostratigraphic units are based on time of deposition
May not follow lithostratigraphic units
  Chronostratigraphic model layers reflect structure of basin
Preliminary

## Slide 11: Why a new framework model?
Chronostratigraphic layers can better represent flow direction
  Captures the orientation of deposits
  Useful when there is high vertical anisotropy
Water level measurements showed a need for a framework model with more layers
Preliminary

## Slide 12: Data Used in Chronostratigraphic Model
Borehole geophysical logs
Water chemistry data
Seismic cross sections
Preliminary
Preliminary

## Slide 13: Geophysical Logs
Data types
  Lithology
  Resistivity
  Spontaneous potential
  Gamma
  Nuclear magnetic resonance
Data used to
  Identify boundaries between layers
  Identify sediment type
Quality of data varied from well to well
Preliminary
Preliminary

## Slide 14: Seismic Cross Sections
Seismic cross sections can show the structure of a cross sectional area
Chronostratigraphic unit boundaries tend follow that structure
Preliminary

## Slide 15: Faulting in New Chronostratigraphic Model
Model includes which layers each fault cuts and the amount each layer is offset
Faults determined from a variety of sources including seismic lines and previous studies
Preliminary

## Slide 16: Grain Size Analysis
Lithology, resistivity, gamma, and nuclear magnetic resonance (NMR) data used to approximate grain size
Lithology
  Gravel and sand coarse
  Silt and clay fine
Resistivity
  Usually higher resistivity in coarser sediments
Gamma
  Usually higher gamma in clays
NMR
  NMR can estimate permeability
Preliminary

## Slide 17: Grain Size Analysis Results
Amount of coarse, medium and fine grained sediment determined
  At each borehole
  For each layer
Preliminary

## Slide 18: Questions Framework Model and Grain Analysis Can Help Answer
How should we layer our groundwater model to best model groundwater flow in the study area?
  How many layers?
  What are the extent of the layers?
  How thick are the layers?
Are there any flow barriers in the model and where should they go?
  Where are the faults and what layers do the faults cut across?
What are the hydraulic properties of our groundwater model?
  How easily does groundwater flow through the different layers?
  How easily does groundwater flow vertically vs horizontally?
Preliminary

## Slide 19: LACP Water Budget
Water spreading
Precipitation and mountain front recharge
Injection
Flow in/out of the study area
Pumping
Preliminary

## Slide 20: Water Spreading
Spreading grounds
  High permeability areas where water percolates into groundwater basins
  Located at San Gabriel River, Rio Hondo, and Whittier Narrows Dam
Preliminary

## Slide 21: Precipitation and Mountain Front Recharge
Recharge estimates from Hevesi and others, 2016
  Done with INFIL
  Modeled both precipitation and mountain front recharge
  Time varying recharge estimates
Hevesi, J.A., and Johnson, T.D., 2016, Estimating spatially and temporally varying recharge and runoff from precipitation and urban irrigation in the Los Angeles Basin, California: U.S. Geological Survey Scientific Investigations Report 2016–5068, 192 p., http://dx.doi.org/10.3133/sir20165068.
Preliminary

## Slide 22: Barrier Injection Projects
Injection at three barrier projects along the coast
  West Coast Basin Barrier Project
  Dominguez Gap Barrier Project
  Alamitos Barrier Project
Preliminary

## Slide 23: Estimated Average Flow In/Out of Study Area (1971-2015)
Estimates based on
  Previous groundwater model
  San Gabriel River Watermaster estimate
Some estimates are better than others
  Orange county boundary estimate
Preliminary

## Slide 24: Pumping by Agency
Four different agency managing pumping in the LACP
  WRD manages the majority of the LACP
Preliminary

## Slide 25: Water Budget Through Time
Pumping fairly constant due to basin adjudication
Water spreading and areal recharge variable
Preliminary

## Slide 26: Questions Water Budget Can Help Answer
How to construct our groundwater model’s boundary conditions?
  Where is groundwater entering and leaving the study area?
  How much water is entering and leaving?
How to model areal recharge?
  How much precipitation is recharging the groundwater basin?
How to model pumping, injection, and water spreading?
  How much pumping, injection, and water spreading is there?
Preliminary

## Slide 27: Summary
LACP is a highly populated area with a significant reliance on groundwater
An understanding of groundwater flow is needed for management of these heavily pumped and complex groundwater basins
Hydrogeologic framework, rainfall, and conceptual models are important first steps to better understanding groundwater flow
These models were used in the construction of an updated groundwater flow model
Preliminary

## Slide 28: Questions?