## Slide 1: Lecture 7
Solute transport modeling

## Slide 2: Solute and Heat Transport
Need to represent solute transport because density is a function of concentration, and concentration may change in response to flow field
Density is also a function of temperature. As temperature increases, density decreases. Temperature may change in response to flow field

## Slide 3: Solute Transport Processes
Physical Transport of solute
  Advection
  Diffusion
  Mechanical Dispersion
Reactive Transport
  Geochemical reactions
  Biological reactions

## Slide 4: Advection
Transport of solute in flowing groundwater with average groundwater velocity
In most cases, advection is primary process for solute transport

## Slide 5: Advective Velocity and Mass Flux
advective velocity
interstitial velocity
pore water velocity
seepage velocity
q: specific discharge (Darcy flux; Darcy velocity)
: “effective” porosity
Velocity of Advective Transport
Advective Mass Flux
Mass per unit time per unit bulk area

## Slide 6: Derivation of Equation for Advective Transport
x
y
z
qxCx
qx+xCx+x
Storage= C/ t
In – Out = Storage
1 Dimension

## Slide 7: Equation for Advective Transport
3 Dimensions

## Slide 8: Dispersion
v  t2
vt1
Spreading of a solute over a greater area than would be predicted solely from average groundwater velocity
Longitudinal dispersion
Transverse dispersion

## Slide 9: Hydrodynamic Dispersion
Molecular Diffusion
Mechanical Dispersion

## Slide 10: Molecular Diffusion
Spread of solute caused by concentration gradients
(A) Container with saline water and distilled water separated by a glass plate
(B) Ionic distribution after removal of glass plate
(C) Ionic distribution at time t1 after removal of plate
(D) Final ionic distribution

## Slide 11: Fick’s Law of Diffusion
F: diffusion mass flux
D*: effective diffusion coefficient [L2/T]
D0: molecular diffusion coefficient in open water
t: is the tortuosity, defined as the length of a sample divided by the length of a flow path through a sample (t < 1)

## Slide 12: Mechanical Dispersion
Spreading of solute as a result of differences in actual velocity and average velocity
Pore Scale
Macro Scale

## Slide 13: Representation of Mechanical Dispersion in Transport Model
By detailed (complete) description of hydraulic conductivity field
By analogy to Fick’s second law of diffusion, i.e., mass flux (F) due to dispersion is proportional to concentration gradients

## Slide 14: Dispersion Coefficients for 1-D Flow in X direction

## Slide 15: Dispersion Coefficients
aL = longitudinal dispersivity
aTH = horizontal transverse dispersivity
aTV = vertical transverse dispersivity
D* = molecular diffusion coefficent
Originally from Burnett and Frind (1987), and currently used in MT3DMS

## Slide 16: Values of Longitudinal Dispersivity
Source: Gelhar et al. (1992)

## Slide 17: Dispersivity Ratios
Source: Gelhar et al. (1992)

## Slide 18: Derivation of Equation for Dispersive Transport
x
y
z
Fx
Fx+x
Inflow=Fxq
Outflow=Fx+Dxq
Storage= C/ t
In – Out = Storage
1D and v is aligned with x axis

## Slide 19: Advection-Dispersion Equation
Assumptions
  v and D are spatially uniform
  v is aligned with x axis
  no sinks/sources
DSP
ADV

## Slide 20: Governing Equation for Solute Transport
ADV
DSP
SSM
RCT
Or, as in MT3DMS
ADV
DSP
SSM
RCT

## Slide 21: Validity of the Advection-Dispersion Model
Dispersion should only be used to account for solute spreading caused by small-scale, randomly distributed heterogeneities in the hydraulic conductivity field. Larger K trends should be explicitly delineated and included in the flow model.

## Slide 22: Alternative to Advection-Dispersion Model
Dual-domain (dual-porosity) mass transfer
1. Fractured flow system
2. Heterogeneous porous media
matrix
fracture
sand
clay
silt

## Slide 23: Dual-Domain Mass Transfer Approach
Aquifer is conceptualized as consisting of two distinctive and overlapping domains:
  a mobile (or fast) domain where transport is mainly by advection, and
  an immobile (or slow) domain where transport is mostly by diffusion
Interaction between the two domains is characterized by kinetic mass transfer
Immobile domain
Mobile domain

## Slide 24: Dual Domain Equations
qm = porosity of mobile domain
qm = porosity of the immobile domain
= qm + qim = total porosity
= first-order mass transfer rate between the mobile and
immobile domains

## Slide 25: Single-Species Chemical Reactions
Sorption
  Mass transfer (or partitioning) process between the contaminants dissolved in groundwater (solution phase) and the contaminants sorbed on porous media (solid phase) including absorption (incorporation into the interior of a solid); adsorption (attraction to a surface); and ion exchange
First-order rate reactions
  Radioactive decay
  Biodegradation
  Hydrolysis

## Slide 26: Equilibrium-Controlled Sorption
Key assumptions
  LEA (local equilibrium assumption)—mass transfer (partitioning) process is instantaneous
  Reversible—total mass is not changed
Retardation concept
  Advancing contaminant plume appears “retarded” because dissolved contaminants are sorbed on to porous materials, leaving less solute for transport
  Retreating contaminant plume appears “retarded” because sorbed contaminants are de-sorbed into the dissolved phase, leaving more solute behind

## Slide 27: Sorption Isotherms
Linear sorption
Freundlich sorption
Langmuir sorption
Nonequilibrium sorption

## Slide 28: Freundlich and Langmuir Isotherms
Dissolved Concentration
Sorbed Concentration
a<1
a=1
a>1
Freundlich isotherm. A linear isotherm is a special case for which the exponent, a, is equal to 1.
Dissolved Concentration
Sorbed Concentration
a=1
A Langmuir isotherm where S is the maximum sorption capacity
S

## Slide 29: Method for Including Sorption into Transport Model
Retardation Coefficient

## Slide 30: 1st-Order Irreversible Rate Reactions
relation between rate coefficient [T-1] and half life [T]
Rate coefficient for dissolved species
Rate coefficient for sorbed species

## Slide 31: Zero-Order Reactions
Rate coefficient for dissolved species
Rate coefficient for sorbed species
g1 [ML-3T-1] and g2 [MM-1T-1] are the zeroth-order rate coefficients for the dissolved and sorbed phase. Positive rate coefficients indicate decay; negative values indicate growth.

## Slide 32: Heat/Energy
Stored
Conducted
Dispersed
Convected
Produced/Lost
Key parameters
  Thermal conductivity (kT)
  Specific heat capacity (cP)

## Slide 33: Heat Capacity
Heat is stored in the fluid and solid
Heat capacity of the fluid and solid represented as: &
Energy stored in fluid:
Energy stored in the solid:

## Slide 34: Heat/Energy Transport
Fourier’s law for heat transport:
Heat is conducted through fluid and solid
Thermal conductivity of the fluid and solid represented as: &
Bulk thermal conductivity:

## Slide 35: Heat Flux
Dispersive heat flux:
Convective heat flux:
Produced/Lost (reaction):

## Slide 36: Heat/Energy Transport (conserve Energy/Mass)
Stored
Conducted and Dispersed
Convected
Sink/Source
RCT(produced/lost)

## Slide 37: Factor out for minimal change in density
…and remember
Production and decay
are distributed sources/sinks

## Slide 38: Equation simplified to…
Substitute:
And substitute the Thermal Distribution Factor:
And substitute the Molecular Diffusion Coefficient:

## Slide 39: Heat transport…
Solute transport…