## Slide 1: Lecture 8
Introduction to MT3D

## Slide 2: MT3DMS File Structure
Basic Transport Package
Advection Package
Dispersion Package
Sink/Source Mixing Package
Reaction Package
MODFLOW to MT3DMS link file
GCG Solver Package
Basic Output File
Model Configuration File [mt3d.cnf]
Unformatted Concentration File [mt3d001.ucn]
Observation File [mt3d001.obs]
Mass Summary File [mt3d001.mas]
MT3DMS
INPUT
OUTPUT
Courtesy Chunmiao Zheng
Transport Observations Package
Hydrocarbon Spill Source – v. 5.3

## Slide 3: Measurement Units in MT3DMS
Length and time units must be consistent with MODFLOW
Concentration units are arbitrary as long as the following points are kept in mind:
  Output concentration unit is the same as the input concentration unit
  The mass budgets calculated by MT3DMS based on inconsistent concentration unit must be converted if absolute mass value is important
  Consistent units must be used if nonlinear reaction is simulated
Courtesy Chunmiao Zheng

## Slide 4: Linkage Between MODFLOW and MT3DMS
Key assumption for standard MT3DMS applications: density change caused by solute transport is negligible
The LMT Package: LMT is a MODFLOW package that saves advective velocities and source/sink flux information needed by MODFLOW
  LMT saves information at the end of every MODFLOW timestep
Courtesy Chunmiao Zheng

## Slide 5: Temporal Discretization
Stress periods
Flow timesteps
Transport timesteps
STRESS PERIOD 2
time
STRESS PERIOD 1
STRESS PERIOD 3
ts1
ts1
ts2
ts3
ts1
ts2
ts3
ts4
ts5
1
2
3
4
5
1
2
3
4
1
2
4
3
1
2
4
3
1
1
1
2
1
2
1
2
3
Transport timesteps

## Slide 6: Steps for Running MT3DMS
Run MODFLOW
  Activate LMT to save flow information (not necessary for SEAWAT)
Create MT3DMS input data files using text editor or preprocessor
Run MT3DMS
Post process
Courtesy Chunmiao Zheng

## Slide 7: Typical Model Results of Interest
Breakthrough concentration curves at specified observation points
Plan or cross-sectional concentration contour maps
Courtesy Chunmiao Zheng

## Slide 8: MT3DMS Packages
Basic Transport (BTN)
Advection (ADV)
Dispersion (DSP)
Source-Sink Mixing (SSM)
Chemical Reaction (RCT)
Generalized Conjugate Gradient (GCG) Solver
Transport Observations Package (TOB)
Hydrocarbon Spill Source Package (HSS)

## Slide 9: BTN Package
Purpose: to specify
  Basic information
  Spatial discretization
  Boundary and initial conditions
  Printing and saving options
  Temporal discretization
Courtesy Chunmiao Zheng

## Slide 10: BTN Package (cont.)
Model Layer Type (Laycon):
  =0: confined layer
   0: unconfined or convertible
Implications
  LAYCON=0: user-specified DZ used as saturated thickness
  LAYCON  0: MT3D determines saturated thickness internally (using MODFLOW approach)
Courtesy Chunmiao Zheng

## Slide 11: BTN Package (cont.)
HTOP: top elevation of 1st model layer
  If top layer is confined, the HTOP values correspond to the actual top elevations of layer 1
  If top layer is unconfined, HTOP can be set to arbitrary values, but keep in mind:
    (HTOP – DZ1) = BOT1 (bottom elevation of layer 1 as specified in MODFLOW)
    Concentration for top layer is calculated midway between HTOP and BOT1
Courtesy Chunmiao Zheng

## Slide 12: BTN Package (cont.)
IBOUND vs. ICBUND
  Active cells in MODFLOW (IBOUND > 0) may be defined as inactive cells in MT3D
  Inactive cells in MT3D – set ICBUND=0
  IBOUND≠ICBUND to exclude active flow cells from transport calculations and speed up transport computation
Courtesy Chunmiao Zheng

## Slide 13: BTN Package (cont.)
Temporal Discretization
  If flow model is steady-state and has ONLY one stress period, transport model can have as many stress periods as necessary, with any desired length for each stress period
  For all other situations, the number of stress periods (NPER), the number of flow timesteps in each stress period (NSTP), and the timestep multiplier (TSMULT) must be identical in flow and transport models
Courtesy Chunmiao Zheng

## Slide 14: Basic Transport (cont.)
For each stress period
  PERLEN (same as in MODFLOW)
  NSTP (same as in MODFLOW)
  TSMULT (same as in MODFLOW)
  TSLNGTH(NSTP) (only for flow model other than MODFLOW)
  DT0: maximum allowable transport stepsize
  MXSTRN: maximum number of transport steps within one flow timestep
  TTSMULT: transport stepsize multiplier within a flow-model timestep
  TTSMAX: maximum transport stepsize within a flow model timestep (set to zero for no limit)
Courtesy Chunmiao Zheng

## Slide 15: ADV Package
Purpose
  To solve the advection components of the transport equation using one of the following options (through input variable MIXELM)
    Finite Difference
      Upstream weighting
      Central-in-space weighting
    Particle-Based Methods
      MOC
      MMOC
      HMOC
    TVD
Courtesy Chunmiao Zheng

## Slide 16: Selection of Solution for ADV
Finite-Difference Method
  Efficient and sufficiently accurate for problems with Pe < 2 to 4
  For problems with Pe > 4, lead to numerical dispersion (upstream weighting) or artificial oscillation (central-in-space weighting)
  Good option for initial test runs to make sure input/output all set properly; should produce negligible mass balance error (<0.1%)
Particle Based Methods
  For problems with Pe > 4 and relatively uniform grid
  Select MOC for pure advection or strongly advection-dominated problems; otherwise, select HMOC
  Mass balance error within 10%
TVD
  For problems with Pe > 4 and for which MOC/HMOC cannot produce satisfactory results (too large mass balance errors or too ‘rough’ breakthrough curves)
Courtesy Chunmiao Zheng

## Slide 17: ADV Package (cont.)
Allowable stepsize for advection
  The courant number, Cr (input variable PERCEL) controls the number of cells any particle is allowed to move during one transport step:
  MOC, MMOC, HMOC: Cr1 (generally set to 1.0)
  Explicit Finite Difference, or TVD Cr 1 (generally set between 0.5 and 1.0)
Courtesy Chunmiao Zheng

## Slide 18: ADV Package (cont.)
In MT3DMS, a fully implicit finite-difference option is available to solve the advection term without any stepsize limitation. However, for accuracy reasons, the Courant number should not be much greater than one, if the problem is advection dominated.
Only when the implicit finite-difference option is used for advection do the following two input variables take effect:
  TTSMULT: transport stepsize multiplier
  TTSMAX: maximum transport stepsize
Courtesy Chunmiao Zheng

## Slide 19: ADV Package (cont.)
MOC
  ITRACK =1 generally ok (1st order)
  =2 generally overkill (RK4)
  =3 suggested (combination)
  WD 0.5  WD  1.0
  = 0.5 generally ok
  =1.0 for purely advective transport
  DCEPS =10-5 generally ok
  NPLANE =0 (random pattern) generally ok
  =1 for 2D plan
  =2 or 3: cross section or 3D
  NPL =0 generally ok, may be as many as NPH
  NPH 16 generally ok for 2D
  NPMIN 32 generally ok for 3D
  NPMAX set about 2 x NPH
  SRMULT =1
MMOC
  INTERP =1 only option available
  NLSINK =NPLANE generally ok
  NPSINK =NPH generally ok
HMOC
  DCHMOC =1x10-3 generally ok
Courtesy Chunmiao Zheng

## Slide 20: DSP Package
Purpose: to solve the dispersion component of the transport equation, using the finite-difference technique
Explicit scheme is subject to a maximum transport stepsize of
Implicit scheme has no stepsize limitation
Courtesy Chunmiao Zheng

## Slide 21: DSP Package (cont.)
AL (longitudinal dispersivity, unit L)
  Cell-by-cell
  2D array for each model layer
TRPT (ratio of horizontal transverse dispersivity to longitudinal dispersivity)
  One value per model layer
  Input as 1D array for all layers
TRPV
  One value per model layer
  Input as 1D array for all layers
DMCOEF
  One value per model layer
  Input as 1D array for all layers
  D*=tD0
Courtesy Chunmiao Zheng
Can now enter different DMCOEFF for each species (starting in version 5.2)

## Slide 22: DSP Package (cont.)
Literature review (see Zheng and Bennett, Chap. 9)
Things to consider
  More heterogeneity in flow model, smaller dispersivities in transport model
  Scale dependent
  Rule of thumb:
    TRPT: 0.1 – 0.01
    TRPV: 0.01 – 0.001
  Temporal variations can account for significant amount of dispersion
  Is dual domain more appropriate?
Courtesy Chunmiao Zheng

## Slide 23: SSM Package
Purpose: to solve the source and sink components of the transport equation
With explicit finite difference method, subject to stepsize stability constraint
Note: qs is sink/source volumetric flow rate divided by cell volume
Implicit scheme can be used to solve SSM component without stability constraint
Courtesy Chunmiao Zheng

## Slide 24: SSM Package (cont.)
Specify hydraulic sinks/sources
  Point sinks/sources
    Constant-head cells (ITYPE=1)
    Wells (ITYPE=2)
    Drains (ITYPE=3)
    Rivers (ITYPE=4)
    General-head boundaries (ITYPE=5)
    …
    Mass loading (ITYPE=15)
  Distributed sinks/sources
    Recharge
    Evapotranspiration
Courtesy Chunmiao Zheng

## Slide 25: SSM Package (cont.)
What is MXSS?
  The maximum number of POINT sink/source cells (including constant-head cells) used in the flow model. It is only used for memory allocation purposes
How does MT3D know about the cell locations and flow rates of sinks/sources
  Through the flow-transport link file saved by the LMT package in MODFLOW
Courtesy Chunmiao Zheng

## Slide 26: SSM Package (cont.)
Time-varying constant-concentration cell (ITYPE=-1)
  This overrides constant-concentration condition as defined in the BTN input (ICBUND<0)
  Once a cell is defined as ITYPE=-1 it remains a constant concentration cell, but a new concentration value can be specified in different stress periods
Mass-loading source cell (ITYPE=-15)
  Users specify Q*C directly (MT-1)
Courtesy Chunmiao Zheng

## Slide 27: SSM Package (cont.)
Specify concentrations of sinks/sources
  Sinks
    By default, concentration of all sinks set equal to that of aquifer at sink/cell locations
    Default concentration of all sinks cannot be changed except for evapotranspiration
  Sources
    By default, concentration of all sources set equal to ZERO unless specified by user
Courtesy Chunmiao Zheng

## Slide 28: SSM Package
Constant-head vs. constant concentration
  A constant-head cell in MODFLOW is treated as a regular fluid sink/source (like a well). The new inflow/outflow rate through the constant-head cell is determined internally by MODFLOW
  If the constant-head cell acts as a source (inflow), the source concentration is zero unless specified by the user in SSM input. If it acts as a sink (outflow), the sink concentration is always equal to that of the aquifer
  A constant-head cell can be specified as a constant-concentration if so desired
Courtesy Chunmiao Zheng

## Slide 29: RCT Package
Equilibrium-controlled linear and non-linear sorption
  Linear Isotherm
  Freundlich Non-Linear Isotherm
  Langmuir Non-Linear Isotherm
Non-equilibrium sorption
  1st order reversible kinetic reaction
Linear Isotherm can be used to simulate thermal exchange between water and solid matrix (see Chapter 11 of v 5.3 manual)

## Slide 30: RCT Package
Radioactive decay or biodegradation
  First-order irreversible rate reactions
Dual-domain Mass Transfer
  Advection dominated transport in fractures and/or high hydraulic conductivity zones (mobile domain)
  Diffusion dominated in low hydraulic conductivity zones filled with immobile or relatively stagnant water (immobile domain)
Zero-order reactions
  Simulation of groundwater age and parameter sensitivities (v. 5.1)

## Slide 31: GCG Solver Package
Solve the linear equations resulting from the finite-difference formulation of
  Dispersion, sink/source, and reaction terms
  Advection term, if the finite-difference option is selected
Control parameters
  MXITER
  ITER1
  ISOLVE
  NCRS
  ACCL
  CCLOSE
  IPRGCG
Courtesy Chunmiao Zheng

## Slide 32: TOBS Package
Obtain the calculated concentration at an observation point that does not coincide with a model node
  Observations at the closest node to observation point
  Use bilinear interpolation to calculate results at the observation point

## Slide 33: TOBS Package
Save the calculated mass fluxes at any sink/source location
  Individual sink/source location
  Arbitrary group of sink/source cells (mass flux object)
Calculate residuals errors at observation locations
  Observations can be weighted
  Residuals can be calculated for multiple times – at times closest to specified time or at specific time using TIMPRS in BTN

## Slide 34: HSS Package
Use to simulate the vertical migration of a light non-aqueous phase liquid (LNAPL) contaminant through the unsaturated zone and the formation of an oil lens on the water table
Determines the rate of contaminant mass flux dissolved from the LNAPL to the groundwater

## Slide 35: HSS Package
Application of HSS Package to other problems:
  Use to specify an arbitrary time varying mass loading source or boundary condition
  Can be used to simulate any MT3D time-varying mass loading sources or boundary conditions

## Slide 36: HSS Package
Application of HSS Package to other problems (cont.):
  Prior to v. 5.3, temporal variation of sources and boundary conditions had to be discretized into stress periods defining
  HSS reduces the need to define stress periods to represent temporal variation of sources and boundary conditions
S.P. 1
S.P. 2
S.P. 3
S.P. 1
S.P. 2
S.P. 3